## Slide 1: TASK 2-DEVELOPMENT OF AN IMPROVED SOLAR DISTILLATION STILL
Dr. Wilbert Odem (Advisor)
Banning Burt,
Yiguo Chen,
Chaz Enbody,
Benjamin Shields,
Yang Yang

## Slide 2: Problem Statement
Design a still with the highest efficiency
Design a still that is cost effective
Ensure that the brackish groundwater contaminants are removed
No electricity
Notes: Chen

## Slide 3: Brackish Water Condition
Component | Value
Conductivity | 6100 µS/cm
Sulfate | 3300 mg/L
Chloride | 550 mg/L
Hardness (as CaCO3) | 3000 mg/L
Sodium | 700 mg/L
Calcium | 600 mg/L
Magnesium | 375 mg/L
Silica | 25 mg/L
Strontium | 10 mg/L
Notes: Banning

## Slide 4: Flagstaff

## Slide 5: Flagstaff

## Slide 6: Flagstaff Details
Climate-November,2011-October,2012
Average Maximum Temperature(oF) | 62.5
Average Wind Speed (MPH) | 6.6
Average Sky Cover | 0.2
Average Relative Humidity (%) | 51.7

## Slide 7: Design Matrix
Notes: Chaz

## Slide 8: Energy Requirement
Equation E= m * (u2 – u1)
Thermodynamic properties for water
Water volume 5 gallon
Energy requirement : 45,780 kJ
Temperature (oC) | Pressure (bar) | Internal energy( )
20 | 1 bar | 83.93
 | 1 bar (x=1) | 2506.1
Temperature (oC) | Pressure (bar) | 
20 | 1 bar | 83.93
 | 1 bar (x=1) | 2506.1
Notes:   Yang (E= Energy, in kJ, M= Mass of water, in kg, and U= Internal energy, in kJ/kg)

## Slide 9: Energy Input
Total Energy
Solar radiation: 1000W/m2
Area: 1,152 in2
E = R * A * Nreflection * Nabsorption
Total Energy Input: 2,440kJ/hr
Energy Loss
q = h * A * (TS – T∞)
Total Energy Loss: 345.4kJ/hr
Energy Input: 2,094.6kJ/hr
Notes:   (Where E is energy input in kJ/h, R is solar radiation W/m2, A is area catch the sunlight in m2, Nreflection is mylar reflection efficiency at 0.97 and Nabsorption is pipe absorption efficiency at 0.94)
  (q is the energy loss in kJ/h=, h is the conductivity coefficient in 7.5 W/m2K, A is the surface area of pipe in 0.15 m2, Ts is the pipe surface temperature in 372.5 K and T∞ is the surrounding temperature in 287.15 K)

## Slide 10: Efficiencies/ Benefits of Materials
Copper- High Thermal absorption coefficient (231 BTU/ft-hr-F)
Mylar- Reduces absorption of heat and hot spots (areas where there is an excessive accumulation of heat) Efficiency- .97
One inlet/ one outlet allows for greater efficiency and rate of production (streamlined process).
Due to simplification of distillation process, entire unit can easily be manipulated to optimize solar energy utilization.

## Slide 11: 1st Design
Description
48” Х 24” Х 24”
Wood, Metal Sheet, Mylar, Copper Pipe with Small Holes, Glass Cover, Frame and V-shape Gutter
Issues
No water collected by gutter.
Focal point not optimized
Incorrect application of Mylar
Notes: Banning

## Slide 12: 2nd Design
Description
48” Х 36” Х 24”
Holes at end of copper pipe
G-code utilized for higher accuracy and efficiency
Super-Max Drilling Mill (±0.01 inch accuracy)
Issues
Steady hydraulic flow was difficult to achieve
High losses due to forced thermal convection
Issues involved with condensation and collection
Notes: Ben
Dimensions: 48” Х 36” Х 24”
Same materials except for the gutter
Holes were placed at end of copper pipe
G-code: determine the location of the pipe in a parabolic shapes
G-code is a type of programming language used by the Super-Max Drilling Mill to cut the parabola shape to a ±0.1 inch accuracy.
Hydraulic flow was very difficult.
Improper sealing caused wind to be a large factor when condensation was on the glass
Difficulty collecting the cleaned water

## Slide 13: 3rd Design
Description
48” Х 24” Х 24”
Wood, Metal sheet, Copper Pipe, Mylar, Dripper, and T-Valve, reflux condensing coil
No glass cover
No holes in copper pipe
One inlet, one outlet, steady hydraulic flow
G-code
Notes: Chaz

## Slide 14: Final Design
Condenser

## Slide 15: Final Design

## Slide 16: Final Design

## Slide 17: Set-Up and Maintenance
Materials
Excel-G Code
Water proof paint
Replacement-easy and cheap
Notes: ben

## Slide 18: Materials and Cost
Notes: Ben

## Slide 19: Testing
9:30am on March 12, 2013
45◦F , 10 mph wind speed
Input: 50mL water
Operating time: 36 minutes
Operation result: 10mL of purified water
20mL of Drained Water
Mass Balance: Ceout = (CinQin− CCWoutQCWout) ∕ (Qeout)
Conclusion:
Water condensed is 33.33%,
Water vaporized is 60%.
Cleft is 2.5 Cin
Notes: yang

## Slide 20: Conductivity Testing

## Slide 21: Losses/Issues
Losses occurred due to:
Forced Thermal Convection
Pipe Fittings- hL=K*(v^2/2(g))
Un-even layering of Mylar (reflectivity)
Thermal absorption of surrounding materials (steel)
Notes: banning

## Slide 22: Legal and Regulatory Consideration
Primary Drinking Water Standards
Secondary Drinking Water Standards
Manufacturing Phase
Operating Phase
Waste Stream Treatment
Notes: ben

## Slide 23: Health Issues
Notes: chaz

## Slide 24: Business Plan
Notes: banning

## Slide 25: Practical Improvements
Optimize reflectivity of Mylar
Utilize evacuated solar tubes/ glass pane to reduce losses due to Forced Convection.
Helio-stat
Notes: banning

## Slide 26: References
WERC. 2013. Task 2- Development of an Improved Solar Distillation Unit. Retrieved from http://www.ieenmsu.com/werc-2/design-contest-2013/tasks-2/task-2-solar-distillation-unit/
Practical Action. 2002. Solar Distillation. Retrieved from http://practicalaction.org/s
olar-distillation-1.
National Oceanic and Atmospheric Administration. 2013. National Weather Servic Flagstaff, AZ, Retrieved from http://floodsafety.noaa.gov/view/validProds.php?prod=
CLI&node=KFGZ
Joel Gordes & Horace McCracken. 1985 .Understanding Solar Stills. Arlington, Virginia.
National Weather Service Forecast Office, 2012. Flagstaff, AZ. Retrieved from http://www.nws.noaa.gov/climate/index.php?wfo=fgz.
Michael J. Moran, Howard N. Shapiro, Daisie D. Boettner and Margaret B. Bailey. 2011. John Wiley & sons, Inc. Hoboken, NJ.
Interactive mathematics. 2013. The Parabola. Retrieved from http://www.intmath.com
/plane-analytic-geometry/4-parabola.php
GlobalMarket, n.d. Solar copper pipe (high efficiency). Retroeved from http://solarsupplier.gmc.globalmarket.com/products/details/solar-copper-pipe-high-efficiency-611915.html
Woods Hole Oceanographic Insitution. n.d. Solar Radiation Retrieved from http://www.whoi.edu/science/AOPE/mvco/description/SolRad.html
Cbsalary. n.d 30 Jobs that pay $30 an Hour. Retrieved from http://www.cbsalary.com/salary-information/article.aspx?articleid=72.
Glassdoor. 2013. Engineering Intern Salaries. Retrieved from
University of Florida. n.d. Zoysiagrass. Retrieved from http://gardeningsolutions.ifas.ufl.
Outsidpride.com. n.d. Seashore Paspalum-Sea Spray. Retrieved from http://www.outsidepride.com/seed/grass-seed/seashore-paspalum/seashore-paspalum- grass-seed.html
Chien L et al. (1968) Infantile gastroenteritis due to water with high sulfate content. Canadian Medical. Association Journal, 99:102–104.
US EPA (1999a) Health effects from exposure to high levels of sulfate in drinking water study. Washington, DC, US Environmental Protection Agency, Office of Water (EPA 815-R-99-001).
Copenhagen, WHO Regional Office for Europe, 1978 (EURO Reports and Studies 2).
Office of Environmental Public Health. 1998. Health Effects Information. Retrieved from http://public.health.oregon.gov/HealthyEnvironments/DrinkingWater/Monitoring/Documents/health/calcar.pdf
Acu-Cell Nutrition. n.d. Phosphorus & sodium. Retrieved from http://www.acu-cell.com/pna.html
Office of Dietray Supplements. 2013. Calcium. Retrieved from http://ods.od.nih.gov/factsheets/Calcium-HealthProfessional/
Office of Dietray Supplements. 2013. Magnesium. Retrieved from http://ods.od.nih.gov/factsheets/Magnesium-HealthProfessional/
Acu-Cell Nutrition. n.d. Germanium & Silicon/Silica. Retrieved from http://www.acu-cell.com/gesi.html
Wisconsin Department of Health Services. 2012. Strontium. Retrieved from http://www.dhs.wisconsin.gov/eh/HlthHaz/fs/strontium.htm
IRIS. 2013. Integrated Risk Information System (IRIS) Retrieved from http://www.epa.gov/IRIS/
Notes: banning

## Slide 27: Website
http://www.cefns.nau.edu/interdisciplinary/d4p/EGR486/CENE/13-Projects/WERC%20Solar%20Distillation/
Notes: Chen

## Slide 28: Questions?
Thank You for Listening