## Slide 1: Sinclair Wash Initial Assessment
Sinclair Wash Team

## Slide 2: Team Introductions
Ryan King: Project Engineer-Hydrologist
Hasan Mohammand: Project Engineer
Leah Richardson: Project Manager
Holly Swenson: Engineering Technician
All

## Slide 3: Project Description
Project Boundary
Current Condition
King
* For all pictures: King W. (2014). Sinclair Wash Project. Unpublished Manuscript, CENE 486 Capstone, Northern Arizona University, United States.
Walmart
S Lone Tree Road
Woody Mountain Road
Sinclair Wash
City Limits
Notes: Flows from the northwest base of Woody Mountain, connects to the Rio de Flag near S Lone Tree Road
Very straight and narrow so during any rain, water overflows the confines of the stream allowing water to go any where promoting pooling in random areas (marsh like)
CMPs go under every trail crossing. Due to settling, they are often at the lowest points of the wash so serious pooling occurs right before an right after the inlet structure
Permanent pond structure near the end of our boundary following restored portion of reach. Right before the end of our boundary

## Slide 4: Purpose
  Initial assessment of the Sinclair Wash
    Identifying problem areas
    Initial conditions modeling
  Achieved through
    Surveying
    Analysis
Swenson
Notes: Purpose-to evaluate and analyze the potential of a restoration project along an unhealthy stream called Sinclair Wash.
Operation : This wash is supposed to operate as an ephemeral stream, preserving and continuing a healthy habitat by transporting flood flows, sediment, and nutrients downstream.
Why : When functioning properly, these streams reduce erosion, improve water quality, provide groundwater recharge and aid in floodplain maintenance.
Team goals : The team’s main goal is to use tools such as site visits, surveying, hydrologic analysis, hydraulic analysis, mapping and comparisons to healthy parts of the reach to determine the feasibility of a Sinclair Wash improvement plan which includes: increasing plant diversity, improving the current eco life, saving cultural heritage, extending recreational opportunities and improving the overall function of the stream channel.

## Slide 5: Client, Technical Advisor, Stakeholders
Client: David McKee, City of Flagstaff Storm Management Section
Technical Advisor: Mark Lamer
Stakeholders: Citizens of Flagstaff, Northern Arizona University, Private Property Owners and Environment
Swenson

## Slide 6: Inventory
Type/Structure | Culvert | Inlet | Open Inlets
PVC |  | 3 | 
1-CMP |  | 11 | 
2-CMP | 1 |  | 
3-CMP | 5 | 1 | 
DBC | 6 |  | 
Concrete |  | 4 | 4
Total | 12 | 19 | 4
Determined location and size of all outlet structures in wash
Invasive species
Measured all culverts within city limits
  CulvertMaster for max capacity
  City Specifications
Mohammad

## Slide 7: Survey
Surveyed cross-sections at 5 locations
TOPCOM GR-3 GPS unit
Input into Civil 3D to develop surfaces
  5 alignments
  Surveyed cross-sections served as sample lines
Mohammad
Walmart
Big 5
San Francisco St
University Heights Dr
1
2
3
4
5

## Slide 8: Soil Analysis
Sieve Analysis to classify soil
  Clean sand or clayey sand (USCS)
  Hydrologic Group D: clay sand (USDA)
Pebble Count
  Modified Wolman method
  Grid
  Used to determine Manning’s coefficient, n
King
Chart: Reach 4: Grain Size Distribution
| 4.75 | 2 | 0.85 | 0.42499999999999999 | 0.25 | 0.106 | 7.4999999999999997E-2
Sample 4.1, 4.2 & 4.3 | 0.8388 | 0.61062 | 0.40851 | 0.27333 | 0.17909 | 0.08975 | 0.058663 | 0.00091067
Sample 4.4 & 4.5 | 0.61223 | 0.38965 | 0.21639 | 0.10816 | 0.065541 | 0.035326 | 0.028092 | 0.0017539
Sample 4.6, 4.7, 4.8 & 4.9 | 0.74914 | 0.5081 | 0.33076 | 0.23669 | 0.17618 | 0.10825 | 0.066764 | -0.0018798
Sample 4.10 & 4.11 | 0.93269 | 0.82891 | 0.57261 | 0.40896 | 0.30091 | 0.17086 | 0.11536 | 0.0044319
Sample 4.12, 4.13, 4.14, 4.15 & 4.16 | 0.83872 | 0.59615 | 0.3718 | 0.22911 | 0.15728 | 0.076554 | 0.042931 | -0.0037674

## Slide 9: Hydrologic Analysis
Used ArcMap with 2013 city contours to delineate watershed
18 Sub-basins
City of Flagstaff requirements
  24-hr storm duration for watersheds greater than 1sq mile
  SCS Curve Number Method for soil loss
  SCS Unit Hydrograph
  SCS Type II rainfall distribution
Richardson

## Slide 10: Hydrologic Analysis: SCS Curve Number
Area of each sub-basin
Soil Group D
Curve Number based on type of cover
Richardson
Sub-basin | Area (miles^2) | Curve Number | Notes
1 | 0.02 | 95 | 80% impervious, 20% woods poor condition
2 | 0.04 | 82.35 | 60% open space fair condition, 6% impervious, 37% woods fair condition
3 | 0.05 | 87 | 1/4 acre residential lot sizes
4 | 0.09 | 92 | 50% paved, 50% woods poor condition
5 | 0.07 | 83.26 | 33% park good condition, 12% impervious, 55% woods fair condition
6 | 0.12 | 95.6 | 80% impervious, 20% woods poor condition
7 | 0.37 | 92.4 | 65% parking, 35% woods fair condition
8 | 0.49 | 94.9 | 80% impervious, 15% woods fair condition, 5% park fair condition
9 | 0.32 | 91.7 | 40% road, 60% open space poor condition

## Slide 11: Hydrologic Analysis: SCS Unit Hydrograph
Length of Flow
Average slope of sub-basin
Overland Flow roughness coefficient
Richardson
Sheet Flow
Shallow Flow
Channel Flow

## Slide 12: Hydrologic Analysis: HEC-HMS Results
Peak discharge at “Junction-2”
  240cfs
  Crossing under San Francisco St.
“Reach 4” had highest channel flow
  220cfs
  Flat area before San Francisco St.
Too Low!
Richardson

## Slide 13: Hydraulic Analysis
Channels
  5 sections of the wash
  Imported alignment and sample line data into HEC-RAS
  Manning’s Coefficient varied based on soil analysis
Culverts
  100-year storm for sections at road crossings
  50-year storm for sections at trail crossings
Richardson

## Slide 14: Hydraulic Analysis Results: Channels
Section Surveyed | Location | Average Free-Board for 100-Year Storm (ft)
1 | South part of University Drive | 1.5
2 | Big 5 | 3.5
3 | Walmart | 3.5
4 | East of I-40 | 3
5 | West of San Francisco | 2
Richardson

## Slide 15: Hydraulic Analysis Results: Culverts
Culvert Analysis |  |  |  |  | 
Type | Reach | Crossing Type | Flow Capacity (cfs) | Storm Flow (cfs) | Pass/Fail
CMP | 3 | FUTS | 40.99 | 456.9 | Fail
CMP | 3 | FUTS | 93.02 | 456.9 | Fail
CMP | 3 | FUTS | 4.98 | 456.9 | Fail
CMP | 3 | FUTS | 49.08 | 456.9 | Fail
CMP | 3 | Road | 219.48 | 512.4 | Fail
Box | 4 | Road | 718.07 | 702.4 | Pass
CMP | 4 | Road | 1503.49 | 702.4 | Pass
CMP | 5 | Road | 2521.6 | 887.4 | Pass
CMP | 5 | Road | 1193.57 | 887.4 | Pass
CMP | 6 | FUTS | 31.58 | 791.4 | Fail
Box | 6 | Road | 879.63 | 887.4 | Fail
Box | 7 | Road | 1198.77 | 905.4 | Pass
CMP | 8 | FUTS | 5.68 | 848.3 | Fail
CMP | 8 | FUTS | 43.76 | 848.3 | Fail
Box | 8 | Road | 1513.44 | 951.3 | Pass
King

## Slide 16: Cost of Engineering Services
Total Cost: $40,990
Total Hours: 653
Swenson
Position | Hourly Billing Rate | Total Number of Hours | Cost
Project Manager | $83 | 176 | $14,547
Project Engineer: Hydrologist | $68 | 172 | $11,638
Engineer in Training | $53 | 142 | $7,456
Engineering Technician: Surveyor | $48 | 157 | $7,488

## Slide 17: Broader Impacts
Increased importance placed on restoring wash
Identified health concerns
Building block for future projects involving wash
Swenson

## Slide 18: Acknowledgements and References
Acknowledgements
  Dr. Charles Schlinger
  Mark Lamer
  David McKee
References
  [1] J. Sutter, "Arizona Department of Environmental Quality," 2010. [Online]. Available: http://www.azdeq.gov/environ/water/assessment/download/lg.pdf. [Accessed 2 November 2014].
  [2] G. Hill, T. Hales and B. Aldridge, "Flood Hydrology Near Flagstaff Arizona," U.S. Geological Survey, Tucson, 1988.
  [3] R. Hereford, "Climate History of Flagstaff, Arizona-1950 to 2007," U.S. Geological Survey, Flagstaff, 2007.
  [4] King W. (2014). Sinclair Wash Project. Unpublished Manuscript, CENE 476 Capstone Preparation Northern Arizona University, United States.
  [5] Provided by Client. Watersheds with Reaches.
  [6] C. o. F.-GIS Department, The Rio de Flag Drainage Through the City of Flagstaff with Stream Team Reach Numbers, Flagstaff: City of Flagstaff.