## Slide 1: Free Piston Stirling Cryocooler
Abdulrahman Alazemi, Faiez Alazmi, Ahmad Althomali, Luis Gardetto, John Wiley
Department of Mechanical Engineering, Northern Arizona University, Flagstaff, AZ
Project Goals
References
Acknowledgments
Design Modifications
    Abstract
The Stirling Cycle is a thermodynamic process that was developed by the Scottish inventor Robert Stirling in 1816. In the original engine design, heat is introduced to the system that expands to displace a piston which in turn creates work. This project goal is to reverse the Stirling cycle in order to remove heat from an insulated vessel. Work is added to a closed system by means of a linear motor that actuates a free piston-displacer assembly and removes heat. Industrial applications of Free Piston Stirling Cryocoolers include temperature critical medical transportation, missile guidance electronic cooling systems, liquefying natural gas processes, and space applications. Low power requirements, minimal moving parts, and compactibility make Stirling Cryocoolers ideal for cooling applications in harsh remote settings.
The design goal is to build an experimental model that will explore thermodynamic properties of the Stirling Cycle to be used within Experimental Methods Laboratory ME 495. Project highlights also include:
Display framework designed and assembled.
Motor control center (MCC) programed to provide adjustable speed capabilities.
Touchscreen Human Machine Interface (HMI) integration for easy operation.
Temperature and pressure sensing instrumentation.
Cooling vessel design to maximize heat removal.
Final Design
Testing Procedures and Results
Dr. David Trevas (Client)
Dr. Sarah Oman (Professor)
Mr. David Willy (Technical Advisor)
Mr. Rod Liebie (Electrical Consultant)
Mr. Jason Nakard (Manufacturing Consultant)
Customer Requirements
College of Engineering, Informatics, and Applied Sciences (CEIAS)
Key Manufacturing Processes
Adjustable Speed Capabilities | Transfers Heat from Cooler
Benchtop Compatible Thermal Sciences Laboratory | Operates on 120 Volt Wall Power
Safe to Operate and Adjust Motor Speed Settings | Manufacturable By NAU Machine Shop
Downloadable Data Acquisition | Replaceable Linear Motor
Ability to Change Working Fluid (Air/Helium) | Replaceable Regenerator Material
Figure 1. Turning outer shell component with heat fins on lathe.
All cooler parts custom manufactured using NAU Fabrication Shop lathe for turning and boring procedures. Precision bolt hole alignment performed using Tormach 1100 CNC machine provided by Transmission Guitars fabrication shop.
Figure 2. Bolt pattern drilling using Tormach 1100.
Figure 3. Final motor cooler assembly. Exploded view to show internal parts.
Motor Housing Cap
Motor Housing
Linear Motor
Motor Mount
Piston
Piston Shaft
Displacer
Inner Cylinder
Regenerator Material
Heat Fins
Outer Shell
Outer Shell Cap
Figure 6. Temperature VS Time
Figure 7 Coefficient of Performance
Figure 4. Final CAD assembly
Figure 5. Final Design assembly
The testing procedures were conducted by plugging in and operating the Stirling cooler. The cooler has an integrated human machine interface (HMI) that allows for the user to specify the duty cycle and frequency. Temperatures were recorded by using the MAX6675 library on the Arduino Integrated Development Environment (IDE) platform. A 24 V power supply was used to adjust the power delivered to the motor.
Test Parameter | Implementation
Motor Speed Adjustment | Touchscreen HMI Adjustment of Stroke Frequency and Pulse Length
Variable Voltage Input and Amperage Monitoring | Utilization of Adjustable Power Supply 0-30V, 0-5 Amps
Pressure Testing | Compressed Air Addition and Leak Check With Soapy Water
Temperature Change | Arduino Interface with LCD Readout. K-type Thermocouples.
Data Collection | Arduino IDE Platform Converted to Microsoft Excel
Coefficient of Performance | COP = Qc/Watts
Parameter Setting | Translation
Time Between Strokes: 15 ms Pulse Length: 20 ms | Duty Cycle: 62.5% Frequency: 25 Hz
Voltage: 24 V Amperage: 0.4 Amps | Cooling Capacity: 9.6 Watts
Initial Pressure: 80.16 kPa | Final Pressure: 89.16 kPa
Ambient Temperature (T1): 22.3 deg C Fin Temperature (T2): 23.0 deg C Cold Head Temp (T3): 23.0 deg C | T1 (Avg): 22.7 deg C T2 (Max): 29.3 deg C T3 (Min): 18.3 deg C
Existing COP: 1.1 [1] | COP: 0.13
Modifications to overall design include:
Piston/Cylinder clearance decreased from 0.008 in to 0.003 in.
Shaft diameter reduced from 0.375 in to 0.187 in.
(Effectively increasing piston surface area by 20%.)
Displacer reconstructed in PVC rather than aluminum.
Table 2. Test Settings and Result Interpretations
Table 1. Testing Parameters and Implementation Methods
Results of operational testing are displayed in Table 2. Temperature reduction of only 4.4 ºC was achieved after nearly an hour of operation. This resulted in a coefficient of performance (COP) of 0.13. Lower results are due to inefficient operation of the system. Compared to existing designs that obtain much larger temperature reductions (-40 ºC) and a higher COP (1.1). [1]
“TWINBIRD Free Piston Stirling Cooler / ABOUT FPSC,” Free Piston Stirling Cooler. [Online]. Available: http://fpsc.twinbird.jp/c/about_fpsc.php. [Accessed: 29-Nov-2018].