## Slide 1: Boeing Autonomous Drone Capstone Northern Arizona University (NAU) 2022-2023

## Slide 2: Introductions
Students
  Dante Faria – Project Manager
  Colby Murphy – Finance and Logistic Manager
  Tommy Schreiber – CAD Engineer
  Damien Brothers – Manufacturing Engineer
  Jay Khunt – Test Engineer
Faculty/Course Advisors
  David Willy
  Armin Eilaghi

## Slide 3: Project Summary
Purpose: Design, analyze, and manufacture a 3D printed drone frame that minimizes weight and maximizes flight time using set commercially available components.​
Sponsor: Boeing
Required Deliverables:​
  Material Optimization​
  Lightweight Prototype
  Central CoM
  Software Stress Simulation

## Slide 4: Requirements
Lighter than 3 pounds
Power to weight ratio improved from 1.81
Durable
Increased flight time
ANSYS/SOLIDWORKS stress simulations
Requirements being met through evaluation of prototype

## Slide 5: Dog Bone Testing
Markforged Mark Two (12 x 5 x 6in)
  Created 20 ASTM D638 Type 1 Dog Bones
  Printed Horizontally
  50% Infill
  Internal Reinforcement
Instron 3385H
  Smaller Clamps Installed

## Slide 6: Dog Bone Testing Results
Strength Rankings
  Carbon Fiber
  HSHT Fiberglass
  Kevlar
  No Reinforcement
Extension Length Rankings
  No Reinforcement
  HSHT Fiberglass
  Kevlar
  Carbon Fiber
No Reinforcement
HSHT Fiberglass
Carbon Fiber
Kevlar

## Slide 7: Final Prototype
Current prototype is not final
Next will look similar with different materials
Frame is 2.2 pounds
Current prototype is 6.03 pounds

## Slide 8: Demonstration 4- Success
Damien, 11
Tested drone in controlled environment (inside) for ~10 successful times before taking outside.
Successful flights in outdoor environment for ~5 times with minimum steering before crash.
  Needed Positioning of components for more stability and achieve the required Center of Mass
Mode: Stability

## Slide 9: Demonstration 5- Failure
Catastrophic Failure about 20 feet above the Concrete
Broke 2 propellers, 1 arm, 2 legs, and 2 Trusses
Most likely the propeller came loose off the motor and caused it to death wobble
Other Issues include:
  Safety mode returning motors to idle
  Lack of control when trying to steer
Dante, 12

## Slide 10: Schedule Update
~75% Complete Build
Next Steps
  Print Final Parts
  Wire Management
Next Deliverables
  U-grads Poster Draft (March 31st)
  Final Testing Plan (March 31st)
Upcoming
  Final CAD Packet (April 7th)
  Final Report (April 21st)
  Final U-grads Poster/Presentation (April 21st)
U-Grads Seminar (April 28th)

## Slide 11: Q&A